## Slide 1: CSS 422 Hardware and Computer Organization
68000 instruction decomposition
Professor: Yang Peng
The slides are re-produced by the courtesy of
Dr. Arnie Berger and Dr. Wooyoung Kim

## Slide 2: Topic
68000 Instruction Set Architecture
  Instruction Set Decomposition
  68K manual
  Chapter 8 (Berger)
  Chapter 2, 3 (Clements)

## Slide 3: Instruction Decomposition
Assemble (decompose): Translate assembly code to machine code
  Why need assembling?
    The memory system can store binary numbers only
    Basically, all assembly languages should be translated into a set of binary numbers to be stored or understood by the computer system
Disassemble: Translate machine code to assembly code
  Why need disassembling?
    It helps you understand assembly programming
    You may need it in your future work
      Software engineer in software security related area

## Slide 4: 68000 Instruction Format
Instruction set in a memory
  Assembly codes are assembled into binary numbers and stored in memory
  One instruction code can be up to 5 words – 80 bits
    10 = 2 + 4 + 4
      For example,
      MOVE.B #14, D0  103C 000E (machine code in hex)
      MOVE.W $0010AA00,$00103000  33F9 0010AA00 00103000
    The first 16-bit (e.g., $103C, $33F9) of an instruction is called the Opcode Word
  contains all of the information needed to decode the rest of the instruction
  contains the Opcode and Effective Address (EA) fields
The complete instruction in memory must contain the opcode word and may contain additional words to complete the instruction

## Slide 5
Example: Only op-code word
  Generally represented as OPCODE
  Example:
MOVE.B D3, D0  1003
EVEN BYTE ODD BYTE
7 6 5 4 3 2 1 0 7 6 5 4 3 2 1 0
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
OP CODE WORD
FIRST WORD SPECIFIES OPERATIONS AND MODES
It is a MOVE.B instruction
The source operand is register D3
The destination operand is register D0
SOURCE EFFECTIVE ADDRESS EXTENSION
IF ANY, ONE OR TWO WORDS
Not used
DESTINATION EFFECTIVE ADDRESS EXTENSION
IF ANY, ONE OR TWO WORDS
Instruction Format in Memory

## Slide 6: Instruction Format in Memory (2)
Example: an immediate operand is the actual data value
  Generally represented as OPCODE #DATA (min. unit is word)
  Example:
MOVE.B #14, D0  103C 000E
OP CODE WORD
FIRST WORD SPECIFIES OPERATIONS AND MODES
SOURCE EFFECTIVE ADDRESS - IMMEDIATE OPERAND
IF ANY, ONE OR TWO WORDS
DESTINATION EFFECTIVE ADDRESS EXTENSION
IF ANY, ONE OR TWO WORDS
It is a MOVE.B instruction
The source operand is immediate data
The destination operand is register D0
The immediate data value, $000E
Not used
7 6 5 4 3 2 1 0 7 6 5 4 3 2 1 0
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
EVEN BYTE ODD BYTE

## Slide 7: Instruction Format in Memory (3)
OP CODE WORD
FIRST WORD SPECIFIES OPERATIONS AND MODES
SOURCE EFFECTIVE ADDRESS
HIGH ORDER WORD
SOURCE EFFECTIVE ADDRESS
LOW ORDER WORD
It is a MOVE.W instruction
The source operand is absolute address
The destination operand is absolute
address
$0010
$AA00
DESTINATION EFFECTIVE ADDRESS
HIGH ORDER WORD
DESTINATION EFFECTIVE ADDRESS
LOW ORDER WORD
$0010
$3000
Example: an absolute operand is the actual data value
  Generally represented as OPCODE source EA, dest EA
      MOVE.W $0010AA00,$00103000  33F9 0010AA00 00103000
7 6 5 4 3 2 1 0 7 6 5 4 3 2 1 0
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
EVEN BYTE ODD BYTE

## Slide 8: Effective Address
The effective address, EA, determines how the operands of an instruction are to be accessed by the processor
Different types of EA’s determine the processor’s addressing modes
In 68K manual, each instruction has different codes for each EA mode:
  Dn: data register direct: D0, D1, …, D7
  An: address register direct : A0, A1, …, A6
  (An): address register indirect: (A0), (A1), …, (A6)
  (An)+: address register indirect with post-increment
  -(An): address register indirect with pre-decrement
  (d16, An): address register indirect with displacement
  (EA = (An)+ d16)
  (d8, An, Xn): address register indirect with index
  (EA = (An)+(Xn)+ d8)
  (xxx).W: Absolute addressing (word)
  (xxx).L: Absolute addressing (long-word)
  #<data>: Immediate Addressing
  (d16, PC): Program counter with displacement (EA = (PC)+ d16)
  (d8, PC, Xn): Program counter with index (EA = (PC)+(Xn)+ d8)

## Slide 9: Assemble manually?
The processor manual tells you what you need to know!

## Slide 10: Format of the 68000 Instructions Set (1)
Two Operands Operation
E.g., MOVE, MOVEA
MOVE instruction: Move the contents at the memory location specified by the src EA to the memory location specified by the dst EA
It’s opcode word is shown below:
  This information is encoded in the 16 bits of the opcode word
    OPCODE/SIZE = Bit15-12
    Destination Effective Address = Bit11-6
    Source Effective Address = Bit5-0
May have to retrieve additional words from memory to complete the instruction
  Note: Not all instructions have the same form as the MOVE instruction
  Refer the 68K manual
MOVE
dst EA
src EA
15 12 11 6 5 0

## Slide 11: 68K Manual

## Slide 12: 68K Manual

## Slide 13: 68K Manual

## Slide 14: Decomposing the MOVE Instruction
Refer the 68K manual for instruction format
Recall that the MOVE instruction format was shown as:
According to the 68K manual, we can decompose this further to:
Opcode word: MOVE.B D3, D0
opcode
dst EA
src EA
0 0
MSB
LSB
DESTINATION
MODE
SOURCE
REGISTER
SIZE
SOURCE
MODE
DESTINATION
REGISTER
Dest = D0
Source = D3
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
15 12 11 6 5 0

## Slide 15: 68K Manual

## Slide 16: 68K Manual

## Slide 17: Decomposing the MOVE Instruction
Refer the 68K manual for instruction format
Recall that the MOVE instruction format was shown as:
According to the 68K manual, we can decompose this further to:
Opcode word: MOVE.B D3, D0
1003
Dest = D0
Source = D3
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
opcode
dst EA
src EA
15 12 11 6 5 0
0 0
MSB
LSB
DESTINATION
MODE
SOURCE
REGISTER
SIZE
SOURCE
MODE
DESTINATION
REGISTER
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0

## Slide 18: Decomposing the MOVE Instruction (2)
Refer the 68K manual for instruction format
Recall that the MOVE instruction format was shown as:
According to the 68K manual, we can decompose this further to:
Opcode word: MOVE.B #14, D0
Dest = D0
Source = #14
opcode
dst EA
src EA
0 0
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
MSB
LSB
DESTINATION
MODE
SOURCE
REGISTER
SIZE
SOURCE
MODE
DESTINATION
REGISTER
15 12 11 6 5 0

## Slide 19: 68K Manual

## Slide 20: 68K Manual

## Slide 21: Decomposing the MOVE Instruction (2)
Refer the 68K manual for instruction format
Recall that the MOVE instruction format was shown as:
According to the 68K manual, we can decompose this further to:
Opcode word: MOVE.B #14, D0
Finished?
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0
Dest = D0
Source = #14
opcode
dst EA
src EA
0 0
MSB
LSB
DESTINATION
MODE
SOURCE
REGISTER
SIZE
SOURCE
MODE
DESTINATION
REGISTER
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
15 12 11 6 5 0

## Slide 22: Decomposing the MOVE Instruction (2)
Refer the 68K manual for instruction format
Recall that the MOVE instruction format was shown as:
According to the 68K manual, we can decompose this further to:
Opcode word: MOVE.B #14, D0
Finished? No, you need one more word for the number #14
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0
Dest = D0
Source = #14
opcode
dst EA
src EA
0 0
MSB
LSB
DESTINATION
MODE
SOURCE
REGISTER
SIZE
SOURCE
MODE
DESTINATION
REGISTER
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
15 12 11 6 5 0

## Slide 23: Decomposing the MOVE Instruction (2)
Refer the 68K manual for instruction format
Recall that the MOVE instruction format was shown as:
According to the 68K manual, we can decompose this further to:
Opcode word: MOVE.B #14, D0
103C 000E
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0
Dest = D0
Source = #14
opcode
dst EA
src EA
0 0
MSB
LSB
DESTINATION
MODE
SOURCE
REGISTER
SIZE
SOURCE
MODE
DESTINATION
REGISTER
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
15 12 11 6 5 0

## Slide 24: Decomposing the MOVE Instruction (3)
Refer the 68K manual for instruction format
Recall that the MOVE instruction format was shown as:
According to the 68K manual, we can decompose this further to:
Opcode word: MOVE.W $0010AA00, $00103000
Dest = $00103000
Source = $0010AA00
opcode
dst EA
src EA
0 0
MSB
LSB
DESTINATION
MODE
SOURCE
REGISTER
SIZE
SOURCE
MODE
DESTINATION
REGISTER
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
15 12 11 6 5 0

## Slide 25: Absolute Addressing Range
Low 32K bytes accessible by 16-bit word addressing
High 32 Kbytes accessible by 16-bit word addressing
Addresses require
32-bit long addressing
00000000
00007FFF
FFFF8000
FFFFFFFF
Sign Extension

## Slide 26: 68K Manual

## Slide 27: 68K Manual

## Slide 28: Decomposing the MOVE Instruction (3)
Refer the 68K manual for instruction format
Recall that the MOVE instruction format was shown as:
According to the 68K manual, we can decompose this further to:
Opcode word: MOVE.W $0010AA00, $00103000
Dest = (xxx).L
Source = (xxx).L
0 | 0 | 1 | 1 |  |  |  |  |  |  |  |  |  |  |  | 
opcode
dst EA
src EA
0 0
MSB
LSB
DESTINATION
MODE
SOURCE
REGISTER
SIZE
SOURCE
MODE
DESTINATION
REGISTER
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
15 12 11 6 5 0

## Slide 29: Decomposing the MOVE Instruction (3)
Refer the 68K manual for instruction format
Recall that the MOVE instruction format was shown as:
According to the 68K manual, we can decompose this further to:
Opcode word: MOVE.W $0010AA00, $00103000
Dest = (xxx).L
Source = (xxx).L
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
opcode
dst EA
src EA
0 0
MSB
LSB
DESTINATION
MODE
SOURCE
REGISTER
SIZE
SOURCE
MODE
DESTINATION
REGISTER
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
15 12 11 6 5 0

## Slide 30: Decomposing the MOVE Instruction (3)
Refer the 68K manual for instruction format
Recall that the MOVE instruction format was shown as:
According to the 68K manual, we can decompose this further to:
Opcode word: MOVE.W $0010AA00, $00103000
Finished?
Dest = (xxx).L
Source = (xxx).L
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
opcode
dst EA
src EA
0 0
MSB
LSB
DESTINATION
MODE
SOURCE
REGISTER
SIZE
SOURCE
MODE
DESTINATION
REGISTER
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
15 12 11 6 5 0

## Slide 31: Decomposing the MOVE Instruction (3)
Refer the 68K manual for instruction format
Recall that the MOVE instruction format was shown as:
According to the 68K manual, we can decompose this further to:
Opcode word: MOVE.W $0010AA00, $00103000
33F9 0010AA00 00103000
Dest = (xxx).L
Source = (xxx).L
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
opcode
dst EA
src EA
0 0
MSB
LSB
DESTINATION
MODE
SOURCE
REGISTER
SIZE
SOURCE
MODE
DESTINATION
REGISTER
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
15 12 11 6 5 0

## Slide 32
The MOVEA instruction is a special form of the MOVE instruction and is used if the destination (dst) is an Address Register
MOVEA.W and MOVE.W have the same opcodes

## Slide 33: MOVEA Notes
Why providing both MOVEA and MOVE?
  In a 68K processor, word accesses must be aligned on word boundaries
  If the same instruction was used to store data in an address register, it would be possible to store an odd address value and cause a non-aligned access to occur
  A runtime error will happen!
MOVE.W #1110, D1 -> Valid according to 68K manual!
MOVE.W #1110, A1 -> Invalid according to 68K manual!
  The destination register of MOVE operation cannot be Address Register
  The Easy68K simulator has a bug that can accept this operation!

## Slide 34: Format of the 68000 Instructions Set (2)
Use an internal register as the source or destination of the operation (i.e., ADD, AND, CMP)
opcode
register
src or dst EA
op mode
15 12 11 9 8 6 5 0

## Slide 35
Effective Address field—
If the location specified is a source operand, all
addressing modes can be used
If the location specified is a destination operand, only
memory alterable addressing modes can be used
Specifies any of the eight data registers

## Slide 36: Exercise
1. Assemble by hand the following assembly language MOVE and ADD instructions
MOVE.B (A0) ,D7
MOVE.L $1234,D7
MOVEA.W D7,A0
ADD.W D0,D7

## Slide 37: Exercise - Illegal Instructions
Explain why the following codes are illegal
MOVE.W $2233,A5
Answer: A5 is an Address register
MOVE.B #$2233,D6
Answer: #$2233 is a word (2 bytes)
ADD.W D0,#$1000
Answer: #$1000 is an immediate number, which cannot be a destination in ADD operation
MOVEA.B D7,A0
Answer: MOVEA can only operate on Word or Long, but not Byte
MOVEA.W A0,$1234
Answer: Destination must be an Address register for MOVEA operation

## Slide 38: Format of the 68000 Instructions Set (3)
Single operand instructions, i.e., CLR (clear the contents of the dst EA)
  An opcode word + rest of instruction (sometimes do not have)
opcode
register
15 6 5 3 2 0
opcode
JMP (Jump) and JSR (Jump to Sub-Routine) are single-operand instructions
  JMP: Change the value of the Program Counter (PC)
  Next instruction is fetched from <PC>
JSR is a special type of jump instruction
  Replaces <PC> with operand but also saves the current <PC> on the stack
  Can return to starting point with RTS
  Used for interrupt subroutines or ISR’s and function calls
mode

## Slide 39: Format of the 68000 Instructions Set (4)
Branch instructions
  Change the program counter value to a new value if a test condition is true
  Test conditions are represented by the state of the flags in the Condition Code Register (CCR)
    Tests can be, zero, overflow, carry or borrow, negative
opcode
condition
displacement
15 12 11 8 7 0
Destination of the branch is calculated by adding the current value of the program counter to the displacement value in the instruction
  Uses 2’s complement, signed addition

## Slide 40: Format of the 68000 Instructions Set (5)
Inherent addressing: The effect (dst or src) of the opcode is inherently contained in the function of the opcode
  RTS: ReTurn from Subroutine:
    JSR instruction PUSH the return location on the stack
    RTS only needs to POP the <PC> in order to get back from the subroutine
opcode
15 0

## Slide 41: Some Representative Instructions
CLR.B ddst 0100001000dddddd
  Clear (set to zero) the byte of the data destination operand – ddst
BNE displacement 01100110dddddddd
  Branch if the result is Not Equal to zero ( Zero flag = 0 )
BEQ displacement 01100111dddddddd
  Branch if the result is EQual to zero ( Zero flag = 1 )
JMP cdst 0100111011dddddd
  Jump to the address defined by control destination operand, cdst
RTS 0x4E75
  Notice that the RTS instruction does not require an operand